## Slide 1: Rethinking Memory Management in Modern Operating System — Memory optimization using hardware features and application characteristics
Lei Liu (SKL, ICT, CAS)
Talk in Huawei U.S. C.A
2015, 7, 30

## Slide 2: Executive Summary
Background & Motivation
Topic 1: Optimization Memory System by OS Approach
Topic 2: Going Vertical!
Topic 3: SYSMON: Making OS understand it!
Topic 4: Our on-going work (if time permits)

## Slide 3: Background & Motivation

## Slide 4: Organization of shared memory system
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
Chip Boundary
On-chip
Off-chip
...
Shared Memory System

## Slide 5: Interferences on DRAM Banks -- DRAM Conflicts
Bank
Row-Buffer Conflicts
2 times Thrashing of Row 1: increases latency
Row-Buffer
Memory Latency = N*tRC (Caused by Row-Buffer Thrashing) + I/O Latency

## Slide 6: The Performance Lost -- Caused by Inter-thread Interferences
Shared cache[Zhuravlev+,ASPLOS10]
  50% performance degradation
Shared DRAM[Moscibroda+,Security06, Onur]
  Unfair: 1.09x v.s. 11.35x
  System slowdown: 2.9x v.s. 6x
Impact Overall System Performance and QoS Seriously!

## Slide 7: Topic 1: Optimizing Memory System by OS Approaches -- “Horizontal” Memory Policies
Most of the contents are in our PACT-2012 and ACM TACO-2014 Papers.

## Slide 8: Page-Coloring Partitioning Approach
Page-coloring technique has been proposed to partition cache.
Cache Set Bits
00
01
10
11
Four-way Associativity
Cache Sets
Physical address
Frame No.
Page Offset
Thread 1
Thread 2
Thread 3
Thread 4

## Slide 9
Some bits in Page Frame Number (PFN) denotes the bank address
Bank bits in PFN
We could extend page-coloring to partition banks
DRAM Banks

## Slide 10
Banks are colored into diff. groups
Partitioning Banks into Groups
DRAM Banks
Thread 1
Thread 2
Thread 3
Reducing the available amount of banks that one thread can access

## Slide 11: The necessary bank amount
The necessary amount of banks one program
requires is limited
Will this influence performance?

## Slide 12: Overview of Our Mechanism

## Slide 13: Bank-level Partition Mechanism (BPM)
Implementation: adopt page-coloring base BPM in Linux kernel 2.6.32 by modifying its buddy system.
  group free pages into 32 colors.
  Adjust the page allocation algorithm in OS.

## Slide 14: Experiment Environment
  System Configuration
  -- 4-core/8-thread Intel Core i7-860 CPU 2.8GHz
  -- LLC: 8MB/16 ways of associativity
Memory Configuration
-- Micron DDR3-1333
-- 2 Channel, 8 Ranks, 64 Banks
Workloads
  -- 23 benchmarks from SPEC CPU 2006 (Multi-Program)
  -- PARSEC (Multi-Thread)

## Slide 15: Experimental Results
System throughput : 4.7% (up to 8.6%)
Maximum slowdown: 4.5% (up to 15.8%)
Memory Power : 5.2% 
A Software Memory Partition Approach for Eliminating Bank Level Interferences (PACT-2012)

## Slide 16: Extend BPM to BPM+
Reducing the Channel Level interferences
“blindly” interleaving
BPM+, Let each thread use a specific channel
BPM/BPM+: Software-based Dynamic Memory Partitioning Mechanism (ACM TACO-2014)

## Slide 17: Overall System Performance

## Slide 18: Memory Optimization Framework -- Supporting Dyn. and Flexible Scheduler

## Slide 19: BPM/BPM+ and Per-core Bandwidth
BPM(+) is promising for future multi-/many-core platforms that have even less per-core bandwidth

## Slide 20: In What We Win?
A practical software approach for eliminating Bank-level Interferences
-- Without any hardware modification to MC
-- Could be deployed on real system easily
-- Improves both fairness and system throughput
-- Saves energy consumption of memory system

## Slide 21: Topic 2: Going Vertical in Memory Hierarchy -- Exploiting the potential optimization space
Most of the contents are in our ISCA-2014 and IEEE Trans. on Computers-2015 Papers.

## Slide 22: Study the Effectiveness of “Horizontal” Partitioning

## Slide 23: “Horizontal” Partitioning: Cache VS. DRAM -- Programs are from SPECCPU2006
Whether the two horizontal approaches work cooperatively?

## Slide 24: Architecture Features in Modern Multicore Systems
B-/C-/O-Bits in Address Mapping
The address Mapping of Intel i7-860 w/ 8GB Memory

## Slide 25: “Vertical” Partitioning using O-Bits
Cache Set
Cache Line
DRAM Banks
T1 T2 T3 T4
Last Level Cache

## Slide 26: Partitioning Space in Entire Memory Hierarchy
The address Mapping of Intel i7-860 w/ 8GB Memory
Notes: .

## Slide 27: The History of Page-Coloring
--Cross-layer Cooperative Vertical partitioning

## Slide 28: The Performance Gains on Vertical Partitioning

## Slide 29: They are in the quadrant ONE
How to obtain the workloads’ sensitivity at runtime?

## Slide 30: How to Leverage the Potential Optimization Space? -- Combining Application’s Memory Patterns and Hardware Features

## Slide 31: What affects Vertical Partitioning?
Cache sensitivity impacts VP
LLCH: Last Level Cache High Requirement LLCT: LLC Thrashing
LLCM: LLC Middle Requirement CCF: Core Cache Fitting

## Slide 32: The Classification of SPECCPU2006
Diverse memory features on Cache and DRAM

## Slide 33: Data Mining: Classification  Best-Fit Partitioning
Algorithm: Using APRIORI algorithm to discover A  B
Modeling：{lib, mcf, bzip, hmmer} 
{<lib, LLCT>, <mcf, LLCH>, <bzip, LLCM>, <hmmer, CCF>}
 <cache-only, x%>, <bank-only, y%>, <A/B/C-VP, z%>

## Slide 34: Handling Multiplicity by Multi-policy -- Memory Policy Decision Tree
Who is “stronger”：LLCT > LLCH > LLCM > CCF

## Slide 35: Supporting Partitioning and Coalescing -- Real Case: “Curve-Vertical” Partitioning
2xLLCT (e.g. 462.Lib, causing cache thrashing)
4xLLCH or LLCM (e.g. mcf, astar.)
*Principle1*: To isolate LLCT applications since it will interfere other application seriously.
*Principle2*: The number of DRAM Banks one application will use is limited.
15~20% performance benefits, outperforming Cache-/Bank-only “Horizontal” partitioning
IEEE Trans. on Computer-2015

## Slide 36: Topic 3: SYSMON -- Making OS understand the memory patterns

## Slide 37: SYSMON: Cache Utilization, Hot/Cold Page, Memory Footprint
It detects __access_bit in PTE, and then distinguishes “cold” and “hot” pages.
It indicates the max requirements of Cache utility of one thread by counting the number of “hot” pages.

## Slide 38: SYSMON: Profiling Page-Level Re-use Time
Lower is better

## Slide 39: SYSMON: “Locality” and “Hot” Freq.
Better Locality
Low access Freq.

## Slide 40: SYSMON: Random Sampling
-- To Handle application with Large Footprint
-- Lower sampling overhead,
but Similar results.
-- Runtime Sampling
-- Easy to be developed
-- Diverse platforms
5~10% PTE is enough to reflect the memory behavior

## Slide 41: SYSMON: Classification based on Sampling Results
Weighted Page Distribution “Locality”
WPD= (2xVH + 1.5xH +1xM + 0.5xL + 0.1xVL) / all_used_pages_num

## Slide 42: Let it Run On-the-Fly! -- Multi-Policy Framework: Supporting Diverse Memory Allocating Policies

## Slide 43: Experimental Results
Horizontal, Vertical, Random (HVR) Framework outperforms the “Horizontal” Partitioning
More experimental results can be found in our paper.

## Slide 44: Conclusion
Horizontal and Vertical Partitioning
-- Brings up to 21% improvement
-- Outperforms the Horizontal partitioning
Closing the “gap” between arch. and OS
-- Makes OS take advantages of arch. Features
-- Application-Arch.-Aware Memory Management (HVR)
Memory optimization
-- We try to approach it from OS angle
-- Optimizes the memory allocating/organizing in the root